## Slide 1: Unit 3. Multi-Path Fading
Ece-gy 6023. Wireless communications
Prof. Sundeep rangan

## Slide 2: Fading
From the Introduction of a classic text:
There are two fundamental aspects of wireless communication that make the problem challenging and interesting.
…First is the phenomenon of fading … …Second …there is significant interference …

## Slide 3: Learning Objectives
Describe up and down-conversion in time- and frequency-domain
Describe the steps in the DAC and ADC including the filtering
Compute a discrete-time and continuous-time base equivalent channels from the passband
Simulate fractional delays and gains in the sampled data
Describe and simulate a deterministic multi-path wireless channel
Compute the time-varying frequency response given the path parameters
Describe a statistical model for multi-path fading
Approximately compute the coherence time and bandwidth given a channel

## Slide 4: Outline
Review of Up- and Downconversion
Review of TX and RX Sampling
Doppler and Multi-Path Fading
Statistical Descriptions of Fading

## Slide 5: Up- and Downconversion
RF communication systems:
  Information occurs and is processed in complex baseband
  Transmitted and received in real passband
Up and down-conversion: Shift center frequency of signals
Also called mixing
upconversion
downconversion
0
f
-
Complex baseband
f
0
Real passband

## Slide 6: Up and Down-Conversion in Time Domain
Complex baseband:
  Two real signals,
  Or one complex signal:
upconversion
downconversion
Real passband:
Note: downconversion needs:
Multiplication by 2
Low pass filtering

## Slide 7: Mixing in Frequency Domain
Baseband signals
  Centered around complex
  single sided bandwidth
  two sided bandwidth
  Band-limited to
Passband signals
  Centered around real
  bandwidth (per side or image)
  Band-limited to
0
A
0
A/2

## Slide 8: Discrete IQ Mixer
LO = “local oscillator” = square or sine wave at
I1, I2 = I and Q inputs.
  Generally, lowpass
RF = passband output centered at
Datasheet | RF [GHz] | LO [GHz] | IF [MHz] | Conversion Loss [dB] | Image Rejection [dB] | Amplitude Deviation [dB] | Phase Deviation [Degrees] | Isolations L-R [dB] | Isolations L-I [dB]
IQ-0318 | 3 to 18 | 3 to 18 | DC to 500 | 7 | 22 | 0.75 | 10 | 40 | 20
http://www.markimicrowave.com/Mixers/IQ_Quadrature-IF_Double-Balanced/IQ-0318.aspx

## Slide 9: Baseband Equivalent Channel
Filtering at passband equivalent to complex baseband filter
Assuming downconversion filter is ideal:
  Simply shift to the left by .
Upconvert
Downconvert
Filter
Filter
=

## Slide 10: Important Special Case: Delay
Delay, gain in passband delay, gain and phase rotation in baseband
Proof:
  Passband frequency response is:
  Baseband frequency response:
  Equivalent impulse response:
Passband channel
gain delay
Baseband equivalent channel
gain delay
= phase rotation

## Slide 11: Synchronization and Delay Errors
Time synchronization at the receiver:
  Estimate the arrival time of the signal
  Starts processing remainder of signal starting at
  Equivalent to shifting received signal ahead in time by :
  Remaining time error:
Later, we will discuss:
  How to estimate (synchronization) and how to correct for gain and phase error (equalization)
Delay estimate
Shift
Delay & gain
0
Sync

## Slide 12: In-Class Problem

## Slide 13: Frequency Errors
Oscillators at TX and RX always have some mismatch. To analyze, suppose:
  Upconversion:
  Downcoversion: )
LO error leads to time-varying gain:
  Frequency and phase shift
LO 1
LO 2

## Slide 14: In-Class Problem

## Slide 15: Outline
Review of Up- and Downconversion
Review of TX and RX Sampling
Doppler and Multi-Path Fading
Statistical Descriptions of Fading

## Slide 16: Typical Digital Communication Path
All modern communication systems TX and RX digital samples
Transmitter: DAC + filtering with . Filtering used to:
  Suppress out of band emissions
Receiver: Filters with then performs ADC. Filtering plays two roles:
  Reduces noise
  Remove out-of-band signals before ADC. (i.e. Anti-aliasing)
Filter design discussed in digital communications class
Ideal A/D
Ideal D/A
TX samples
RX samples

## Slide 17: Review of DTFT
Given discrete-time sequence
  Real or complex
Discrete-time Fourier Transform:
Inverse DTFT:
Note is always a periodic signal
  Can take integral for inverse DTFT on any period of
is the discrete frequency. Units is radians per sample.
For finite length signals and finite number of , can be computed via FFT
Review in your signals and systems class

## Slide 18: Common DTFT Pairs
See Wikipedia

## Slide 19: Discrete-Time Systems
Consider discrete-time LTI system
Time-domain: Characterized by impulse response
Frequency-domain: Characterized by frequency response

## Slide 20: DT Equivalent Channel
Discrete-time baseband equivalent channel:
  Describes equivalent mapping from to
  Includes effects of TX and RX filtering and continuous-time baseband channel
Band-limited filters:
  Suppose one of is bandlimited to (no out-of-band emissions or aliasing)
  Then, discrete-time equivalent channel reduces to: for
ADC
DAC
=

## Slide 21: Ideal Filtering
Suppose sample rate
“Ideal” TX and RX filter :
  In frequency domain:
  Also called “brick wall” filter
Most practical filters match this well
  Up to gain and delay
ADC
DAC
=

## Slide 22: Ideal Filtering
Assume TX and RX filters are ideal
Theorem: DT equivalent channel is the re-scaled continuous-time channel
  Frequency mapped to
ADC
DAC
=

## Slide 23: Special Case: Delay
Suppose passband has a gain and delay.
Then discrete-time frequency-domain: gain and linear phase rotation over frequency
  Rotates radians every period
In discrete-time time-domain: gain, constant phase rotation and sinc filter with delay
 | Passband | Continuous-Time Baseband | Discrete-Time Baseband
Impulse response |  |  | 
Frequency response |  |  | 
 | Passband | Continuous-Time Baseband | Discrete-Time Baseband
Impulse response |  |  | 
Frequency response |  |  | 

## Slide 24: Sinc Filter with Integer Delays
Suppose we have ideal filtering and passband has delay and gain
From previous slide,
Special case 1: No delay
  Baseband channel introduces only gain
Special case 2: Integer delays
  Baseband channel introduces gain and integer shift
Ex: Suppose sample rate is 20 MHz and signal is delayed by 400 ns.
  Integer delay in discrete-time signal is samples

## Slide 25: Sinc Pulses with Fractional Delay
Causes blurring over multiple samples
Inter-symbol interference
Will need equalization to correct
  More on this later

## Slide 26: Simulating Fractional Delays in MATLAB
Code on previous slide was create with DSP toolbox
Creates T x D matrix
Row is delayed by

## Slide 27: In-Class Problem: Fractional Delays on Constellations

## Slide 28: Outline
Review of Up- and Downconversion
Review of TX and RX Sampling
Doppler and Multi-Path Fading
Statistical Descriptions of Fading

## Slide 29: Doppler Shift
With mobile velocity, propagation delay changes with time.
In complex baseband signal:
Velocity results in Doppler shift:
Change in frequency, although not gain.
Mobile velocity

## Slide 30: Sample Problem
Suppose the carrier frequency is =2.1GHz, and a car moves towards a base station at 100 km/h. What is the Doppler shift?
Answer: v=100km/h= m/s, c= m/s,
If the angle is
v=100 km/h

## Slide 31: Multipath Channel
Most channel consists of many paths
  Direct paths
  Reflections, transmissions, diffraction, …
  LOS and NLOS paths
Each path has different
  Delay
  Phase
  Gain

## Slide 32: Baseband Model
TX sends complex baseband
RX receives complex baseband:
  paths
  Gain and phase:
  Complex gain:
  Delay:
  Doppler:

## Slide 33: Time-Varying Frequency Response
Multipath channel:
Consider exponential input:
Output is:
Time-varying frequency response
May also write:

## Slide 34: Example with Two Paths
To simplify understanding, consider two path model
Time-varying response:
Power gain:

## Slide 35: Variation in Time
Plot shows =10 Hz, ,
Fixed frequency
Look at time variations
Rate of variation depends on Doppler spread:
Size of variation depends on spread of gains:
  Avg:
  Min: : Destructive interference
  Max: : : Constructive interference
With equal path gains, there are nulls

## Slide 36: Variation in Frequency
Fixed frequency
Look at time variations
Period of variation depends on delay spread:
Size of variation depends on spread of gains:
  Avg:
  Min:
  Max:
Plot shows ns, ,

## Slide 37: Fading
Over time and frequency, paths can either
  Constructively interfere Peaks
  Destructively interfere Nulls
Process is called fading
  Intermittent channel quality
One of the most significant challenges in wireless
Later, we will discuss how to overcome fading

## Slide 38: Narrowband Assumption
For two path model:
Period of variation in =
Suppose that has bandwidth
Narrowband assumption valid when
is the delay spread
Represents max difference in path lengths

## Slide 39: OFDM Time-Frequency Grid
OFDM modulation: Widely-used method
  4G and 5G cellular systems
  Many 802.11 standards
Divide channel into sub-carriers and OFDM symbols
  Resource element: One time-frequency point
Data is transmitted is an array:
  OFDM symbol index
  = subcarrier index
  One complex value per RE.
  Called a modulation symbol
See digital communication class
  We will also review again when we discuss equalization
Subcarrier spacing
OFDM symbol
Time
Frequency

## Slide 40: OFDM Channel with Fading
OFDM channel acts as multiplication: Under normal operation (delay spread is contained in CP):
OFDM channel gains can be computed from the multi-path components
  OFDM symbol time, sub-carrier spacing
  For each path: Doppler shift, Delay, phase of path, path received energy
RX symbols
Channel
TX symbols

## Slide 41: Summary
Doppler to a single path causes a phase rotation
  Gain is constant
With multiple paths, gain varies
  Constructive and destructive interference of paths
Described by a time-varying frequency response
  Variations is time due to Doppler spread
  Variations in frequency due to delay spread

## Slide 42: In-Class Exercise: OFDM Channel Response

## Slide 43: Outline
Review of Up- and Downconversion
Review of TX and RX Sampling
Doppler and Multi-Path Fading
Statistical Descriptions of Fading

## Slide 44: Random Path Statistical Model
RX signal has many random, independent paths
Time-varying frequency response:
  Assume ) i.i.d.
  Path gains: are zero mean
By Central Limit Theorem, is a complex Gaussian
  Independent real and imaginary components
  Variance for real and imaginary components
Direction of motion

## Slide 45: Rayleigh Distribution
complex Gaussian
magnitude
Represents amplitude gain
Has Rayleigh distribution:
  PDF:
  CDF:
  Second moment:
Probability distribution

## Slide 46: Exponential Distribution
Consider Rayleigh fading complex gain
Magnitude is Rayleigh
Instantaneous gain has exponential distribution
  Average gain is
For channel, represent power gain (in linear scale)

## Slide 47: Example Calculation
Suppose the channel experiences Rayleigh fading.
What is probability gain will be 15 dB below the average?
  Called a 15 dB fade.
Answer:
  Gain is 15 dB below average when
  From exponential distribution:
  For small ,
  For 15 dB fade,

## Slide 48: Winner-3GPP-Spatial Cluster Model
Paths arrive in clusters.
Clusters have subpaths (also called rays)
Each cluster has:
  Center angle and a statistical model for the delay and angular spread
From 3GPP SCM-132

## Slide 49: Jakes Model
Many widely-used statistical models in practice
Some specify models with no delay spread
  Angular spread only
  Creates a time-varying gain
  No variation in delay
  Use one of these models per cluster
Jakes model:
  Angles uniform from
Asymmetric Jakes:
  uniform
Angular spread:
  Arises from diffuse reflection
Jakes
Angles unif
Asym Jakes
Asym Jakes
Gain (dB)
Angle (rads)

## Slide 50: Fading Models in MATLAB
Comm Toolbox:
  Efficient, general fading models
Create a comm.RayleighChannel object
Run the channel to get:
  Output and gain

## Slide 51: Doppler Spectra
Consider statistical model:
  Paths are i.i.d. and are zero mean
In limit of large , is a Gaussian random process
Auto-correlation:
Describes how correlated the process is over time and frequency

## Slide 52: Coherence Time and Frequency
Consider time varying freq response
Coherence time:
  Max interval where
  How fast channel changes in time
  Related to Doppler spread
Coherence bandwidth
  Max interval where
  How fast channel changes in frequency
  Related to delay spread
Critical for many procedures:
  Channel estimation, tracking, coding, ARQ, …
  More on this later
Realization of a Jakes process with 1/fmax = 0.1 sec

## Slide 53: Fading at Different Scales
Source of variation | Mathematical model | Typical spatial coherence | Typical temporal coherence
Small-scale fading from multi-path fading | Rayleigh or Rician distribution | ~ 1 wavelength | 15 ms (v=10m/s, fc=2GHz)
Large-scale fading from variations in shadowing | Lognormal distribution | 10 to 100 m | 1 to 10 sec
Path loss variations | Path loss exponent | 100 m or larger | 10 sec
Different fading processes and variations occur at much different time / space scales
Methods to combat these are different

## Slide 54: Time Scales Illustrated